UEET101: Introduction to Engineering

Spring 2007

Group 6

Reverse Engineering a Blender

Timothy Pearson, Team Lead

Objective

The objective of this project is to glean information about the design of an ordinary kitchen blender through dissection.  Various engineering design aspects will be examined, and ways to improve the product will be proposed.  The outcome of this project should be to improve the product where necessary.

Introduction

The blender is a relatively simple kitchen appliance with many different uses, from pureeing fruit to crushing ice and milling grain.  To accomplish these tasks, a high-powered electric motor is used to spin metal blades at the bottom of a container.  While in use, the blades push ground food to the sides of the container.  This results in a whirlpool action that continually brings unground food into the rotating blades.  We will examine certain engineering challenges present in the design of this device below.

Mechanical Engineering Analysis

The electric motor assembly is mounted on four vibration dampers in the upper housing.  The vibration dampers allow the entire motor assembly to move slightly in order to keep the motor’s shaft aligned with the blade assembly at all times.  This prevents binding of the motor’s shaft, as well as keeping vibration to a minimum.  There is a large bearing in the motor assembly that keeps the main shaft properly aligned within the field coils while the motor is in operation.  A small slide bearing on the other end of the shaft near the brushes also helps to align the main shaft.

In order to keep the motor from overheating during a period of extended use, a metal fan is mounted on the shaft just below the brush assembly and slide bearing.  It is offset from the slide bearing by a small spacer, and secured with a locknut.  The slide bearing--when the spacer, fan, and locknut are mounted--constrains the shaft vertically, preventing the shaft from moving up and down.

To transfer power from the motor to the removable blade assembly, a four-sided output shaft is attached to the motor’s shaft directly above the large bearing.  The output shaft sticks up about a half inch beyond the upper housing, allowing it to mate with a similar socket on the blade assembly.  A small, flat, round disk is present just below the output shaft and above the upper housing.  This acts to protect the bearing from any loose food or other debris that could otherwise fall into the space between the output shaft and the upper housing.

The blades are secured into the food container by means of a retaining ring.  There are slots formed into the upper housing of the blender, into which tabs on the ring lock.  This holds the ring, blades, and food container in place on the top of the blender.  The retaining ring screws onto the bottom of a food container, thus allowing multiple food containers to be used with the blender.

Electrical Engineering Analysis

The electric motor is a standard wound-rotor induction motor.  Individual switches are for speed control, and vary the connections to the field coils.  The ‘hot’ lead from the plug passes through a fuse and connects directly to one of the brushes.  Current passes through the wound rotor and out to the other brush.  From there, current passes through the field coil that is selected by the switch bank and back out to the neutral wire of the plug.  The carbon brushes are spring-loaded, so as to allow a good electrical contact even in the presence of wear.

Industrial Engineering Analysis

This blender, while high quality, is designed for ease of manufacturing.  The case is molded plastic, and many of the metal parts, such as the fan, are stamped.  The most complex components to manufacture appear to be the wound rotor assembly and the switch bank.

Possible Improvements

In this design, there is a chance of the operator becoming injured when removing the blades from the food container.  It might be a good idea to make the blades permanently affixed to the retaining ring, so that the operator would never need to come in close proximity to the exposed blades.  Other than that, this seems to be a powerful, well-constructed blender, designed to last a very long time.